## Slide 1: ALiCoFSS
REVIEW 2
Problem definition, requirements, literature survey, concept and project plan
Multidisciplinary project | EEE | Civil | AI/ML

## Slide 2: The problem
1 PROBLEM IDENTIFICATION AND DEFINITION
Lift and Coast (LiCo) saves fuel and reduces brake and tyre wear, and skilled racing drivers use it routinely. But it demands mastery and precision, so an average driver cannot do it consistently. Done badly, it is also a safety risk to the driver and the people around them.
What it is
Lift off the throttle early and let the car slow itself, instead of braking late.
The barrier
It takes judgement of distance and vehicle behaviour that most drivers lack.
The risk
Done wrong, it is a safety risk for the driver and people nearby.

## Slide 3: Who is affected, and when
1 PROBLEM IDENTIFICATION AND DEFINITION
Who
Everyday ICE drivers. IC vehicles will remain a large share of the fleet for years.
Situation
Approaching a sharp junction turn where speed must drop substantially, for example 40 to 15 km/h.
Typical driver
Holds speed, then brakes hard about 10 m before the turn. Wastes fuel and wears brakes.
Lift and coast
Lifts off 200 to 500 m before the turn, depending on the vehicle and scenario. The car slows without braking.
vs

## Slide 4: Evidence that the problem is real
1 PROBLEM IDENTIFICATION AND DEFINITION
Racing practice
Lift-and-coast is a routine fuel-saving technique in racing. In a Le Mans Ultimate test at Spa, one lap saved nearly 1.5 L for about 0.7 s lost [9]. An iRacing guide puts consistent use at about 5 to 10% less fuel per stint [10].
Our own runs
In sim racing, one team member's own runs show roughly 2 to 3 L saved per Nürburgring lap with lift-and-coast versus flat out. This is informal and not yet logged.
Ordinary roads
Eco-driving that anticipates curves and slows smoothly used less fuel than human-style driving in simulation [1]. Human drivers slow quickly, then re-accelerate.
Racing figures are simulator-based, from sim-racing sources: indicative, not validated. We will measure our own savings in simulation.
Notes: Be upfront: the racing figures are simulator-based, from sim-racing sources, not real race data. The 2-3 L per Nurburgring lap is the presenter's own informal observation and is not logged. The road-relevance evidence is the eco-driving paper (Bakibillah et al.), which compares anticipatory driving with human-style driving in simulation. We commit to measuring our own savings in simulation.

## Slide 5: What already exists and the gap
1 PROBLEM IDENTIFICATION AND DEFINITION
Curve-based eco-driving
Model-predictive control on gradual road curvature and surface conditions [1][2].
Eco-approach at signals
Uses traffic-signal timing from connected infrastructure to avoid stops.
ALiCoFSS
GPS and map only. Sharp junction turns. Lift-and-coast replaces braking.
The gap: we did not find existing work that replaces braking with lift-and-coast at sharp junction turns, using only GPS and map data, and adapting to the vehicle's condition.

## Slide 6: Scope of the project
1 PROBLEM IDENTIFICATION AND DEFINITION
In scope
Simulation only, in CARLA
Throttle and brake only; driver input always overrides
Sharp junction turns on flat roads, nominal 40 to 15 km/h
One base vehicle, then a few variants such as degraded brakes or tyres
A small fixed set of surfaces and weather: dry, wet, heavy rain
Out of scope
Real vehicle testing
Steering, which stays with the autopilot or driver
Other vehicles, pedestrians and traffic signals
Camera-based lead-vehicle matching (deferred)
Wind (deferred)

## Slide 7: How success will be measured
1 PROBLEM IDENTIFICATION AND DEFINITION
We are not committing to a target percentage yet, because it depends on a fuel model and baseline we have not validated. What we have defined is how success will be measured.
Metric
Fuel used per turn event.
Baseline
A scripted human-style driver (late, hard braking) on the same route, vehicle and conditions.
Success criterion
A consistent fuel reduction versus baseline across repeated runs and conditions, without missing the turn speed or the safety override.
Target value
Set after baseline runs. No percentage is quoted before then.
Notes: We are deliberately not quoting a percentage target. It depends on the fuel model and baseline, which are not validated yet. The target will be set after baseline runs.

## Slide 8: Functional requirements
2 REQUIREMENT ANALYSIS
1
Read the vehicle's speed and position
2
Know the upcoming turn's location and required speed from map data
3
Decide when to lift off so coasting, not braking, brings the car to turn speed
4
Brake only when coasting alone cannot reach the turn speed
5
Hand control back instantly when the driver uses gas, brake or clutch
6
Log every run for analysis

## Slide 9: Data and simulation requirements
2 REQUIREMENT ANALYSIS
Data to log
Timestamp, position, speed
Throttle, brake, steering
IMU acceleration
Surface friction and weather setting
Fuel, computed from the log
What the simulator must offer
Scripted control and logging through the Python API
Fixed timestep (for example 0.05 s) so runs repeat
Sharp 90° turns on known routes
Adjustable mass, drag, tyre friction and torque curve
Fuel computed offline, as CARLA outputs none

## Slide 10: Performance and safety requirements
2 REQUIREMENT ANALYSIS
Turn speed
Reach the required speed at the turn without braking where possible. Tolerance set after baseline runs.
Deceleration
Stay within a maximum deceleration limit, to be agreed, for comfort and safety.
Driver override
Any gas, brake or clutch input ends the system's control immediately.
Noisy GPS
Define safe behaviour when position data is poor, for example handing control back.
Notes: Tolerances are intentionally not numeric yet. They will be set after baseline runs, consistent with not committing to a target percentage.

## Slide 11: Requirements by discipline
2 REQUIREMENT ANALYSIS
EEE
Provides
Coasting deceleration, logged vehicle data, decision logic.
Needs
Turn and surface classes, ML model output.
Civil
Provides
Turn classes and geometry, friction values per surface.
Needs
Speed and deceleration limits from the vehicle.
AI/ML
Provides
A model that outputs the lift-off decision.
Needs
Logged data in an agreed format, plus vehicle and road inputs.
Inputs and outputs must match at these interfaces.

## Slide 12: Closest prior art: Bakibillah et al.
3 LITERATURE SURVEY
Problem
Slowing for horizontal curves means braking and re-accelerating, raising fuel use and emissions. Existing eco-driving ignores the preceding vehicle and road surface (dry, wet, snow).
Method
Nonlinear MPC computes the optimal speed from vehicle dynamics, the preceding vehicle's state, surface friction and curvature from GPS points.
Limitation
Single-lane car-following only, with no lane changes or overtaking. Lateral dynamics ignored and road inclination assumed negligible.
How ours differs
Learning-based, adapts to vehicle condition. Targets sharp junction turns with lift-and-coast replacing braking. Needs only GPS and map data, not the preceding vehicle's state.
[1] Bakibillah, Kamal, Tan, Hayakawa, Imura. Heliyon 2024;10:e23586 (Elsevier)

## Slide 13: Closest prior art: Heuts et al.
3 LITERATURE SURVEY
Problem
Eco-driving advice ignores road curvature and cornering energy losses, giving dangerously high corner speeds and inaccurate energy estimates.
Method
A cornering loss model inside a convex optimal control problem, solved in the spatial domain. Curvature is estimated from GPS data using osculating circles.
Limitation
Single-vehicle control, with no other vehicles, pedestrians or signals. Relies on static manufacturer vehicle parameters, which causes errors in long-term energy predictions.
How ours differs
Petrol vehicle using lift-and-coast. Learns the vehicle's actual behaviour instead of fixed datasheet values. Targets sharp junction turns, not gradual curvature.
[2] Heuts, Velpari, Donkers. Energy 2025;334:137526 (Elsevier)

## Slide 14: Shared limits and our difference
3 LITERATURE SURVEY
Both papers
ALiCoFSS
Model-based: nonlinear MPC or convex optimisation
Learning-based model that adapts
Fixed vehicle parameters
Adapts to vehicle condition
Gradual road curvature
Sharp junction turns
Heliyon paper only: needs the preceding vehicle's state
Needs only GPS and map data

## Slide 15: Supporting references
3 LITERATURE SURVEY
Reference | Area | Why it matters
[3][4] Ahn et al. 2002, J. Transp. Eng.; Rakha et al. 2004, Transp. Res. D | Fuel model (VT-Micro) | Fuel and emissions from speed and acceleration. Candidate for our fuel model; check how it treats lift-off.
[5] Zamfir et al. 2016, IOP Conf. Ser.: Mater. Sci. Eng. | Road friction | Curve speed limit from surface friction, v = √(μ·g·R), as used in [1].
[6] Beckers et al. 2020, Transp. Res. D | Cornering losses | Shows cornering energy losses should not be ignored.
[7][8] Huang et al. 2024, Applied Energy; Nie and Farzaneh 2022, Energy | Learning-based eco-driving | Model-free methods need substantial training data and retraining for new vehicles, per [2].
[9][10] Coach Dave Delta; iRacerHUB | Lift-and-coast evidence | Simulator-based sim-racing sources. Indicative only.
Items [3] to [8] are cited as listed in [1] and [2].
Notes: Items 1 to 4 are cited as listed in the two prior-art papers. The sim-racing sources are simulator-based and used only as indicative evidence.

## Slide 16: Survey takeaway and next reading
3 LITERATURE SURVEY
What the survey shows
Closest prior art is model-based, with fixed vehicle parameters and gradual curves
The Heliyon paper already compares against human driving and includes road surface, so we do not claim those as new
Our difference: learning and adapting to the vehicle, on sharp junction turns
Still to survey
Driver behaviour and personalisation
Adapting to vehicle condition, sim-to-real
Pavement friction values per surface
Junction geometry and turn radii

## Slide 17: System concept
4 CONCEPT FORMULATION
GPS + map
Position and route. Turn locations come from the map.
Turn and road info
Distance to turn, required speed, surface grip.
ML model
Learns where to lift off from speed, distance, coasting behaviour and grip.
Coast / brake decision
Lift off now, keep coasting, or brake only if needed.
Simulated vehicle
Throttle and brake in CARLA. Steering stays with the autopilot.
Vehicle feedback
Speed, IMU, throttle and brake feed the model.
Driver override
Any gas, brake or clutch input takes control back at once.

## Slide 18: What the model learns and decides
4 CONCEPT FORMULATION
Inputs
Approach speed
Distance to the turn
Required turn speed
Vehicle's coasting deceleration
Road grip
ML model
Outputs
Where to lift off
Coast or brake command
The relationship does not depend on the map. A new map only supplies new turns.

## Slide 19: Physics baseline for lift-off
4 CONCEPT FORMULATION
d = (v₁² − v₂²) / 2a
a is the coasting deceleration: drag, rolling resistance and engine braking
Measured from coast-down tests in CARLA
Example: 40 to 15 km/h with a = 0.25 m/s² gives d ≈ 212 m (illustrative)
Chart: Distance (m), turn at 300
| 0 |  |  |  |  | 50 |  |  |  |  | 100 |  |  |  |  | 150 |  |  |  |  | 200 |  |  |  |  | 250 |  |  |  |  | 300
Late braking | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 15
Lift-and-coast | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 40 | 39.8 | 39 | 38.2 | 37.3 | 36.4 | 35.5 | 34.6 | 33.6 | 32.7 | 31.7 | 30.6 | 29.5 | 28.4 | 27.3 | 26 | 24.8 | 23.4 | 22 | 20.5 | 18.8 | 17 | 15
Illustrative schematic from the formula with an assumed a = 0.25 m/s². Not simulator data.
Notes: The chart is an illustrative schematic generated from the formula with an assumed coasting deceleration of 0.25 m/s2. It is not simulator data. The coast-down test will give the real value for the simulated vehicle.

## Slide 20: Fuel model concept
4 CONCEPT FORMULATION
No native fuel output
CARLA does not report fuel. We compute it from logged speed, throttle and vehicle physics.
Candidate: VT-Micro
A published model that estimates fuel from speed and acceleration [3][4].
Must encode fuel cut-off
A real engine uses almost no fuel when lifting off at speed. Without this, coasting shows no saving.
One model for all runs
The same fuel model scores the baseline driver and ALiCoFSS, so the comparison is fair.
The final choice will be defended after checking how VT-Micro treats deceleration.

## Slide 21: Objectives
5 PRELIMINARY PROJECT PLAN
1
Build a CARLA simulation with sharp-turn routes and logged vehicle data
2
Measure the simulated vehicle's coasting deceleration and define the analytic lift-off baseline
3
Define a human-style baseline driver and one fuel model to compare against
4
Train an ML model that decides lift-off across vehicle states, surfaces and maps
5
Compare fuel per turn event and brake use against the baseline, with the safety override respected

## Slide 22: Methodology
5 PRELIMINARY PROJECT PLAN
1
Set up and log
CARLA with a fixed timestep, GNSS and IMU sensors, and CSV logging.
2
Coast-down tests
Release the throttle from several speeds and log the slowdown. Check for engine braking.
3
Baseline and fuel model
Script a late-braking human-style driver. Fix one fuel model for all runs.
4
Vary conditions
Vehicle variants through physics settings, surfaces through friction, several maps.
5
Train and compare
Train on some maps and conditions, test on held-out. Compare with the analytic baseline.
6
Measure
Fuel per turn event, brake use, turn-speed error and override checks.

## Slide 23: Roles and ownership
5 PRELIMINARY PROJECT PLAN
EEE
CARLA setup and sensor logging
Coasting physics baseline
Fuel model
Decision logic
Civil
Turn and surface classes
Friction values with sources
Turn geometry from road design practice
AI/ML
ML literature review
Model inputs and outputs
Training data format
Adapting across vehicles and conditions

## Slide 24: Progress so far
5 PRELIMINARY PROJECT PLAN
Done: working CARLA demo
Map loaded and car spawned
GNSS sensor attached to the vehicle
Autopilot driving the car
Live speed, throttle, brake and steering values printed
Next
Coast-down test from about 40 km/h
Fixed timestep so runs repeat
Add the IMU and log to CSV
Log a run through a sharp 90° turn
Control values read from the vehicle stand in for reading its control unit in a real car.
Notes: Live demo: map loaded, car spawned, GNSS sensor attached, autopilot driving, speed printed along with throttle, brake and steering values read from the vehicle (a stand-in for reading its control unit). Be ready to say which source the speed comes from.

## Slide 25: Risks and open questions
5 PRELIMINARY PROJECT PLAN
Risk
Plan
Fuel model: CARLA gives no fuel output.
Compute from logs. Test VT-Micro and model fuel cut-off.
Surface and weather: CARLA weather may be mostly visual.
Vary tyre friction directly, using sourced values.
Baseline realism: The autopilot is not a typical human driver.
Script a late-braking driver with some variation.
Evidence quality: Racing figures are simulator-based.
Label as indicative. Measure our own savings.

## Slide 26: References
REFERENCES
Closest prior art
[1] Bakibillah ASM, Kamal MAS, Tan CP, Hayakawa T, Imura J. Optimal eco-driving scheme for reducing energy consumption and carbon emissions on curved roads. Heliyon 2024;10:e23586.
[2] Heuts YJJ, Velpari R, Donkers MCF. Eco-driving and road curvature estimation: Retrospective analysis of experimental data of a fully electric coach. Energy 2025;334:137526.
Supporting, as cited in [1] and [2]
[3] Ahn K, Rakha H, Trani A, Van Aerde M. Estimating vehicle fuel consumption and emissions based on instantaneous speed and acceleration levels. J Transp Eng 2002;128(2):182-190.
[4] Rakha H, Ahn K, Trani A. Development of VT-Micro model for estimating hot stabilized light duty vehicle and truck emissions. Transp Res Part D 2004;9:49-74.
[5] Zamfir S, Drosescu R, Gaiginschi R. Practical method for estimating road curvatures using onboard GPS and IMU equipment. IOP Conf Ser Mater Sci Eng 2016;147:012114.
[6] Beckers CJJ, Besselink IJM, Nijmeijer H. Assessing the impact of cornering losses on the energy consumption of electric city buses. Transp Res Part D 2020;86:102360.
[7] Huang R, He H, Su Q. An intelligent full-knowledge transferable collaborative eco-driving framework based on improved soft actor-critic algorithm. Appl Energy 2024;375:124078.
[8] Nie Z, Farzaneh H. Real-time dynamic predictive cruise control for enhancing eco-driving of electric vehicles (ANN-based energy model). Energy 2022;241:122888.
Simulator-based sources (indicative only)
[9] Coach Dave Delta. Mastering Lift and Coast: How to Save Fuel Without Sacrificing Speed. coachdaveacademy.com/tutorials/mastering-lift-and-coast-how-to-save-fuel-without-sacrificing-speed
[10] iRacerHUB. How to Save Fuel in iRacing GT3 Cars. iracerhub.com/how-to-save-fuel-iracing-gt3/

## Slide 27: Summary
Problem: LiCo saves fuel but takes skill; we automate it for sharp turns
Gap: we did not find work doing this with GPS and map data only, adapting to the vehicle
Next: coast-down tests, baseline driver, fuel model, first logged turn runs
Thank you.